## Slide 1: What Every Hacker Should Know About TLB Invalidation
December 2024
Hackers to Hackers Conference (H2HC)
Paweł Wieczorkiewicz
Open Source Security, Inc.

## Slide 2: PAWEŁ WIECZORKIEWICZ EMAIL: WIPAWEL@GRSECURITY.NET TWITTER / X: @WIPAWEL
Security Researcher at Open Source Security, Inc. (creators of grsecurity®)
Low-level security research of system software and hardware
Reverse engineering and binary analysis
Kernel Test Framework (KTF)
creator and maintainer https://github.com/KernelTestFramework/ktf

## Slide 3: Outline
Theory
  What is TLB?
  What is the purpose of TLB?
  Paging-structure caches demystified
  Basic whys and whens of TLB invalidation
  Optimizations
    Global Pages
    PCID and VPID
  Details of TLB invalidation
Practice
  An interesting case study of a PaX/grsecurity PRIVATE KSTACKS bug
  A case of broken INVLPG instruction on new generations of Intel CPUs

## Slide 4: What is the Translation-Lookaside Buffer (TLB)?

## Slide 5: What is the Translation-Lookaside Buffer (TLB)?
Virtual Memory (VM) and Memory Management Unit (MMU)
  A simplified view:
    Software operates within many various virtual address spaces
    Hardware operates within a single physical address space
      Virtual address != physical address
        Translation is needed

## Slide 6: What is the Translation-Lookaside Buffer (TLB)?
Virtual Memory (VM) and Memory Management Unit (MMU)
  A simplified view:
    Software operates within many various virtual address spaces
    Hardware operates within a single physical address space
      Virtual address != physical address
        Translation is needed
  Paging and page tables
    Implementation “detail” of Virtual Memory
    Physical memory split into frames of standard sizes (4K, 2M, 1G)
    Virtual memory address space split into pages of physical frames sizes
    Physical frames mapped to virtual address spaces to back virtual memory pages
      Extra metadata of virtual memory pages: Present, Read/Write, User/Superuser, …

## Slide 7: What is the Translation-Lookaside Buffer (TLB)?
Example schematic of 4-level page tables
Format of typical 4K virtual memory page
Source: Intel® 64 and IA-32 Architectures Software Developer’s Manual

## Slide 8: What is the Translation-Lookaside Buffer (TLB)?
Virtual Memory (VM) and Memory Management Unit (MMU)
  Paging and page tables – page walk
    Every time a virtual address is being accessed by SW  CPU has to perform a page walk
      CPU has dedicated page walk HW units to perform this process transparently
    A page walk begins by getting physical address of a top page table from a dedicated register (CR3 on x86)
      This table memory has to be fetched, indexed, metadata flags need to be examined
    From the fetched and indexed table next level page table physical address is obtained
      Again, this table memory has to be fetched, indexed, metadata flags need to be examined
    This traversing continues until the lowest level of the page table hierarchy provides actual memory address
    This process is very expensive

## Slide 9: What is the Translation-Lookaside Buffer (TLB)?
TLB is a (set of) cache buffer(s) automatically storing previous, successful page walk results
TLB caches recent virtual address to physical address translations …
  … and a summary of traversed page table entries metadata flags

## Slide 10: What is the Translation-Lookaside Buffer (TLB)?
TLB is a (set of) cache buffer(s) automatically storing previous, successful page walk results
TLB caches recent virtual address to physical address translations …
  … and a summary of traversed page table entries metadata flags
Typical TLB consists of entries referenced by a virtual page number (e.g. virtual address >> 12)
Typical TLB entry consists of:
  Physical frame number (physical address = (frame number << 12) + offset)
  Access rights from page tables’ entries used for the translation:
    Logical AND of Read/Write flags
    Logical AND of User/Superuser flags
    Additional page table metadata attributes

## Slide 11: What is the Translation-Lookaside Buffer (TLB)?
Organization of TLB hardware may differ across various CPU microarchitectures
  TLB can be split into independent: instruction TLB (iTLB) and data TLB (dTLB)
    Different number of entries
      Due to different spatial and temporal characteristics of accesses
    Different metadata flags cached
      For example: code does not need a dirty flag
  Multiple levels of TLB buffers
    For example:
      First level: iTLB + dTLB
      Second level: unified TLB

## Slide 12: What is the purpose of TLB?
Probably obvious at that point  PERFORMANCE
TLB caches recent translations obtained with expensive page walks
  A principle of temporal locality applies:
    Recently used virtual memory page is likely to be re-used again soon
  Each TLB Hit is a huge win
TLB acting as an intermediate cache allows to:
  Pipeline and/or parallelize fast TLB Hits with slow TLB Misses
    Outsource expensive and slow work to hardware page walk units …
    … while keep serving TLB Hits quickly

## Slide 13: TLB quirks and peculiarities

## Slide 14: TLB quirks and peculiarities
TLB caches entries only for successful page walks
  Each page table level entry used for a translation has to have:
    Present flag set
    Reserved bits zeroed
  Intel SDM:
    “the processor does not cache a translation for a page number unless the accessed flag is 1 in each of the paging-structure entries used during translation…”
      Software can use it for deciding if invalidation is needed
    “… before caching a translation, the processor sets any of these accessed flags that is not already 1”
      This can be used for page walk detections
  This obviously affects the need for invalidation

## Slide 15: TLB quirks and peculiarities
Intel SDM: “the processor may cache a translation for any linear address, even if that address is not used to access memory”
  TLB may store for example:
    Translations for memory prefetches
    “accesses that result from speculative execution that would never actually occur in the executed code path”
      Side-channels, side-channels everywhere!
Intel SDM: “On a processor supporting Hyper-Threading Technology, invalidations performed on one logical processor may invalidate entries in the TLBs and paging-structure caches used by other logical processors”
In other words: making assumptions about presence or absence of TLB entries is risky!

## Slide 16: TLB quirks and peculiarities
TLB may cache a huge page (e.g. 2M or 1G) translation as multiple 4K pages translations
  This implementation detail is not visible to software
    It may complicate explicit invalidation requirements for such huge page translation
TLB may contain several distinct translations for the same physical memory addresses at once
  For example:
    TLB contains an existing 4K virtual page translation
    Software modifies a corresponding page table entry, so the virtual page size changes (e.g. 2M)
    Accessing the virtual page now may lead to allocating a completely new TLB entry
  Which entry should be used for subsequent accesses?
    Intel SDM: “Which translation is used may vary from one execution to another, and the choice may be implementation-specific”
      Making assumptions is risky again!

## Slide 17: An introduction to paging-structure caches

## Slide 18: Introduction to paging-structure caches
TLB is not the only cache buffer used for optimizing expensive page walks
Modern CPUs usually implement also caches for higher-level page table entries
  In addition to the TLB’s:
    A memory address final translation
      Obtained from the lowest-level page table entry
    A summary of all-level page table entries metadata flags

## Slide 19: Introduction to paging-structure caches
The principle of temporal and spatial locality applies again:
  Regardless of a TLB capacity and its state, the same higher-level page table entries may be re-used frequently
    Because they participate in mapping larger portions of virtual address spaces…
    … or may be used by cross-address-space mappings of common, shared data (e.g. kernel code, libraries)
Caching them may noticeably improve performance of many workloads on modern OSes
Typically distinct paging-structure caches exists for all higher-level page tables
Caching higher-level page table entries help reduce a page walk cost  performance
  Any cache hit shortens the page walk
    The lower the level  the shorter the page walk necessary

## Slide 20: Introduction to paging-structure caches
Exemplary PDPTE (3rd level page table) cache properties
  Entries indexed with only a part of the virtual address – depending on the paging mode
    Example: 4-level paging mode  bits 47:30, just 18 bits
  Typical cache size is small – depends on a CPU microarchitecture implementation
  Entries contain:
    Physical address of a PDE page table (2nd level page table)
    A summary of this and higher-level page tables entries metadata flags
        Logical AND for: Read/Write and User/Superuser
        … etc
Similar characteristics and properties apply to all other (higher and lower level) paging-structure caches

## Slide 21: Paging-structure caches – more details
Huge pages entries are not cached in paging-structure caches
  1G pages have PS bit set in the 3rd level page table entries
    No need for lower-level page table entries
  2M pages have PS bit set in the 2nd level page table entries
    No need for PTE
  These are handled by TLB
Similarly to TLB requirements:
  Only entries of present and valid (no reserved bits set) pages are cached
  Accessed flags of the page table entries involved in the page walk are set by the CPU

## Slide 22: Paging-structure caches – more details
According to documentation: CPU is free to create a paging-structure cache entry at any time
  Even when there are no translations for virtual addresses using the entry
  Similar to the TLB case:
    “The processor may create entries in paging-structure caches for translations required for prefetches and or accesses that are a result of speculative execution that would never actually occur in the executed code path”
Already created cache entry may remain unmodified regardless of software’s subsequent modifications to the page tables
  Need to explicitly invalidate
Entries are associated with the current PCID – more on this later

## Slide 23: TLB and paging-structure caches interaction
How does CPU use TLB with paging-structure caches?
  In case of a direct TLB hit  TLB entry data is used immediately
  In case of a TLB miss:
    Paging-structure cache for 2nd level page table entries (PDE) may be consulted
      In case of a cache hit  quick page walk (just PTE is needed)
      In case of a cache miss:
    Paging-structure cache for 3rd level page table entries (PDPTE) may be consulted
      In case of a cache hit  shorter page walk (just PDE and PTE needed)
      In case of a cache miss: …
    … and so on depending on the caches available…
  If CPU misses in all the caches  a full page walk is scheduled

## Slide 24: Why and when a TLB invalidation is needed?

## Slide 25: TLB invalidation – why?
In case of a TLB hit:
  CPU may use found TLB entry to determine a page frame, access rights, and other attributes
  CPU will likely NOT consult the page tables in memory
As mentioned earlier:
  “The processor may retain a TLB entry unmodified even if software subsequently modifies the relevant paging-structure entries in memory”
    … and same is true for paging-structure caches!
In other words:
  Invalidation is needed to maintain coherency between translation caches (TLB, paging-structure caches) and page tables in memory at all times
    Without this coherency: system stability and security is gone

## Slide 26: TLB invalidation – when?
Whenever the in-memory page table entries and their potentially cached values might be out-of-sync?
  Excellent guarantees, but terrible performance
Whenever software modifies page tables?
  Not necessarily, remember the requirements for caching (Present bit set, etc)
    Some modifications can assume the entry is not in cache
  Whenever virtual address space changes?
Whenever one process (page table A) is context switched into another process (page table B)?
  What if they share some memory pages?
  What about common kernel code?

## Slide 27: TLB invalidation – when?
Invalidating too much is very bad for performance
  Operating systems try to invalidate only:
    When necessary and …
    … what really needs to be flushed
Invalidating too little however makes performance not matter at all
In real-life situations discussed later, we will see how problematic this can be
  Some optimization assumptions might not hold …
    … and be super complex to reason about
  And… of course… a broken CPU microcode...

## Slide 28: Hardware optimizations

## Slide 29: Hardware optimizations
Hardware features have been added to CPUs in order to:
  Help software maintain the translation cache coherency more efficiently
  Eliminate unnecessary invalidation of frequently used translation entries
The features:
  Global Pages
  Process Context Identifiers (PCID)
  Virtual Processor Identifier (VPID) – virtualization feature (vCPU tagging)
All the features are optional, but can be also used all together
  Most if not all of modern OSes use PCID
  Some of the OSes additionally rely on Global Pages
    Examples: FreeBSD

## Slide 30: Hardware optimizations – Global Pages
Global Pages feature was added to limit unnecessary invalidations of frequently used pages
  For example: shared memory pages between different virtual address spaces
    Common code (libraries)
    Always mapped-in kernel memory
Whenever virtual address space is being changed (on a task switch or process context switch)
  The corresponding page tables have to be changed as well
    Thereby, on x86 a full TLB flush is triggered by:
      All writes to the CR3 register
      A hardware task switch
Flushing and then hitting TLB misses for the same memory accesses is a waste

## Slide 31: Hardware optimizations – Global Pages
Enabling Global Pages feature (PGE bit of CR4 on x86) makes CPU respect addition flag in page table entries
  Global flag (G)
Software can decide what are the shared or frequently used virtual memory pages and mark them as global
  By setting the G bit in their lowest-level page table entry
  Note: there is no G bit for higher-level page table entries
When enabled, TLB entries with a global flag are not invalidated automatically when page tables are reloaded
  Automatic avoidance of TLB misses for shared memory

## Slide 32: Hardware optimizations – Global Pages
However…
  Global pages take up TLB entries
    A good balance is needed to avoid TLB thrashing
  Invalidation of global pages is more complicated
    Might not be worth it, when it has to occur often
Some quirks:
  Global pages do not affect the behavior of paging-structure caches at all
    Only higher-level page table entries cached there
  Global pages entries in TLB might be used by CPU regardless of their specific PCID
    Global means global after all… it’s getting complicated

## Slide 33: Hardware optimizations – Process-Context Identifiers (PCID)
PCID feature was added to limit the need for translations invalidation
It enables software to tag different virtual address spaces with different (almost) unique identifiers
… and thereby allows CPUs to easily distinguish between different virtual address spaces (tag matching)
  CPU can consume cached translations only for the current address space (current PCID)
  No need to invalidate other virtual address space translations proactively
  Hardware will flush translation entries when it needs space for new ones (e.g. using LRU algorithm)
Frequently used translations, even from different address spaces, can remain in the translation caches
  Maintenance simplification
  Big potential performance gain

## Slide 34: Hardware optimizations – Process-Context Identifiers (PCID)
PCID is a 12 bit identifier  up to 4096 different virtual address spaces can coexist
PCID of zero is the default (also: current) one
  Setting PCIDE bit in CR4 register (on x86) enables non-zero PCIDs
The current address space PCID is indicated by the 12 LSB bits of the CR3 register (x86)
  Switching page tables during process context switch allows to specify different PCID
CPU creates entries in TLB and paging-structure caches tagged with the current PCID
  … and uses only those entries that are tagged with the current PCID (unless global)
Hardware-level logical address space translations isolation
Disabling PCID (via unsetting PCIDE bit in CR4) triggers entire translation cache hierarchy invalidation
  PCID of zero becomes again the current and only one PCID

## Slide 35: TLB Invalidation details…

## Slide 36: Operations triggering TLB invalidation
x86 instructions:
  INVLPG <virtual address>
    Invalidates any TLB entry for the specified virtual address and current PCID
    Invalidates any global page TLB entry for the specified virtual address for all PCIDs
    Invalidates all entries in all paging-structure caches for all virtual addresses of the current PCID
  INVPCID <type>, <descriptor>
    Descriptor points at 128 bit memory structure, where virtual address and PCID are specified
    Type operand controls the scope of invalidation:
      (0) Address – invalidates any TLB entry (not global) for the descriptor’s virtual address and PCID
      (1) Single context – invalidates all TLB entries (not global) for the descriptor’s PCID
      (2) All contexts with globals – invalidates all TLB entries for all virtual addresses and all PCIDs
      (3) All contexts – invalidates all TLB entries (not global) for all virtual addresses and all PCIDs
    Invalidates entries in all paging-structure caches according to the type and descriptor operands

## Slide 37: Operations triggering TLB invalidation
Other operations:
  Disabling paging (e.g. unsetting PG bit of CR0 on x86)
    No surprises here – invalidates everything everywhere
  Page table switch (e.g. writing to CR3 on x86)
    With PCID disabled – all TLB (but no globals) and paging-structure caches entries
    With PCID enabled – depends on the MSB (63) bit of the CR3 value
      0 – invalidates all TLB (no globals) and paging-structure caches entries for a new PCID
      1 – no invalidation (utilizing PCID feature isolation capabilities)
  Disabling/Enabling of Global Pages feature
    Invalidates everything everywhere
  Disabling of the PCID feature
    Invalidates everything everywhere

## Slide 38: Operations triggering TLB invalidation
Exceptions:
  Page Fault exception (#PF) also invalidates entries in TLB and paging-structure caches
    #PF exceptions result from accessing a virtual memory address
      Various reasons: page not present, read-only, privilege violation, …
    Upon #PF the following happens:
      TLB entries for the #PF virtual address (stored in CR2 on x86) and current PCID are invalidated
      Only paging-structure caches entries relevant for the virtual address translation and current PCID are invalidated
    #PF induced invalidations are to prevent reoccurring exceptions due to stale translation caches entries
Virtualization transitions (VMEnter and VMExit) also invalidate TLB and paging-structure caches entries

## Slide 39: TLB Shootdown – inter-processor invalidation
TLB and paging-structure caches are typically per logical CPU resources - each logical CPU has their own
On processors with multiple cores and/or supporting hyperthreading coordinated invalidations may be required
  Upon modification of the in-memory page tables multiple CPUs may contain stale translation entries
  Not enough for the page table modifying CPU to invalidate only its own translation caches
  A TLB Shootdown operation must be initiated, so the translation cache hierarchy across all CPUs is in sync
TLB Shootdown:
  Usually implemented using execution barriers and inter-processor interrupts (IPI)
  Procedure overview:
    Initiating CPU before the in-memory page table modification traps all necessary CPU on a barrier
    … modifies the page table and performs its own invalidation
    … signals to the trapped CPUs to perform their invalidation
    All CPUs resume execution

## Slide 40: When software has to invalidate TLB?
Modification of a page table entry mapping a virtual memory page
  Software should issue INVLPG for all related virtual addresses
    One INVLPG per page number is enough
Modification of a page table entry mapping another page table entry
  I.e. modification of a higher-level page table
  Depending on the target page table’s mappings count and their types:
    Many mappings: full invalidation (e.g. via CR3 register write) might be the best choice
    Otherwise, individual INVLPG invalidations for the mappings might be optimal
    Even if there is none – e.g. target page table entries have all pages not present
        Still at least one INVLPG is necessary!
        Why? You will see later…

## Slide 41: When software has to invalidate TLB?
Modification of a page table entry size
  Huge page mapping
  May lead to multiple translations in TLB for the same virtual addresses
    One for the new huge page and one or more for the previous 4K pages
  CPU may use any of the available translations
  To avoid this, software has to first invalidate all affected translations
Page table entry modification write might get re-ordered and get executed after a subsequent memory access
  This can create a stale translation entry
  Invalidation instructions are all serializing instructions

## Slide 42: When software has to invalidate TLB?
PCID identifier re-use
  PCID value space is relatively small (12 bit – 4096 distinct values)
  There may be more than 4096 virtual address spaces running concurrently on a system
  Software has to re-use same PCID for different virtual address spaces
    To avoid collisions in TLB and paging-structure caches:
      Invalidate all translations for the new PCID
      The CR3 bit 63 serves that purpose, but does not invalidate global entries
      For global entries more drastic measures have to be used:
        All context with globals INVPCID
        Disable  Enable Global Pages

## Slide 43: When software does not have to invalidate?
Modification of a page table entry mapping a non-present virtual page
  Translations for non-present pages are not cached (neither in TLB nor paging-structure caches)
  In other words: making a non-present page present does not require invalidation
    Unless the page was present before and no invalidation has occurred since!
Modifying access flag of a page table entry
  0 -> 1 – neither TLB nor paging-structure caches stores translations for untouched entries
  1 -> 0 – without invalidation CPU might not set the flag on a subsequent access – not fatal
Modifying Read/Write flag of a page table entry
  Read-only  Writeable – without invalidation #PF exception may occur
    Not fatal, but sub-optimal
    #PF will invalidate the cached translations
  Writeable  Read-only – fatal without invalidation

## Slide 44: When software does not have to invalidate?
Modifying User/Superuser flag of a page table entry
  User  Superuser – fatal without invalidation
  Superuser  User - without invalidation #PF exception may occur
    Not fatal, but sub-optimal
    #PF will invalidate the cached translations
Modifying dirty flag of a page table entry
  1 -> 0 – without invalidation CPU might not set the flag on a subsequent write – not fatal

## Slide 45: When software does not have to invalidate immediately?
Intel SDM quote: “The processor may retain entries in the TLBs and paging-structure caches for an extended period of time. Software should not assume that the processor will not use entries associated with a linear address simply because time has passed”
Example: unmapping (or remapping) a part of a virtual address space
  Unsetting page table entries Present flag
    Two cases:
      (case 1) Page table entry mapping a page
      (case 2) Page table entry mapping another page table

## Slide 46: When software does not have to invalidate immediately?
What can go wrong without immediate invalidation in general here?
  If OS re-uses the freed portion of the virtual address space
    Stale translation entries point at different physical memory (or with different access rights)
      Immediate fatal consequences
  If OS re-uses the physical memory behind the freed portion of the virtual address space
    Stale translation entries allow to access the same physical memory
      Potentially with different access rights
    “But nothing uses the freed virtual address space, so how bad can it be?”
      Such assumptions usually die fast…
      Speculative execution enters the scene…

## Slide 47: TLB Invalidation – When Software does not have to invalidate immediately?
What can go wrong without immediate invalidation in the case 2?
  Intel SDM: “… the processor may create an entry in a paging-structure cache even if there are no translations for any linear address that might use that entry”
    What does that mean?
      CPU can populate paging-structure caches at its own discretion…
  Also Intel SDM: “if software has marked “not present” all entries in a page table, the processor may subsequently create a PDE-cache entry for the PDE that references that page table”
  One may think that it does not sound too bad…
    Well, let’s see…

## Slide 48: PaX/grsecurity PRIVATE KSTACKS bug

## Slide 49: PaX/grsecurity PRIVATE KSTACKS
What is the PRIVATE KSTACKS feature?
  Private kernel stacks hardening enhancement introduced in PaX/grsecurity around February 2022
    Kernel will disallow access to all process and IRQ kernel stacks except for the ones used by the currently running task on a given CPU
      All-but-current process stacks not mapped
      IRQ handlers cannot view other CPU IRQ stacks
    This defence mechanism:
      Completes the protection by PAX_RAP_RET and PAX_RAP_XOR
      Prevents cross-kernel stack attacks and stack overflow/underflow attacks
      Addresses attack that caused RFG to be shelved, without requiring CET/HW shadow stacks
        Return Flow Guard - Microsoft attempt at backward-edge Control-Flow Integration
        For shelved reason, see slide 27 of The Evolution of CFI Attacks and Defenses

## Slide 50: PaX/grsecurity PRIVATE KSTACKS – Example (without)
Task
Workthread Task
crypto_shash_digest(desc, in_data, len, &outbuf);
Process Stack
Task Struct
Process Stack
retaddr2
retaddr1
Task Struct
retaddr1
char outbuf[32];
calls
Writes to outbuf
Can corrupt retaddr!
But needs to write to outbuf!

## Slide 51: PaX/grsecurity PRIVATE KSTACKS – Example (without)
We have two tasks of many on the system
  A waiting task that just called a synchronous crypto API that will provide a hash digest in its on-stack output buffer
  A running workthread task doing the actual work
Without PRIVATE KSTACKS
  The workthread task needs to write to a buffer on the waiting task’s stack
  But, this also allows bugs existing in that code to corrupt other parts of the other task’s stack
    Including its other local variables or return addresses

## Slide 52: PaX/grsecurity PRIVATE KSTACKS – Example (with)
Task
Workthread Task
Unmapped Process Stack
Task Struct
Process Stack
retaddr2
retaddr1
Task Struct
retaddr1
Can’t corrupt retaddr!
Write to outbuf happens without stack map/unmap
‘Nolocal’ page
char outbuf[32];
crypto_shash_digest(desc, in_data, len, &outbuf);
calls
Writes to outbuf

## Slide 53: PaX/grsecurity PRIVATE KSTACKS – Example (with)
With PRIVATE KSTACKS
  The waiting task’s stack is completely unmapped from the perspective of the workthread task
    The possibility to corrupt the return address or other local variables is gone
  The workthread task still needs to write to the output buffer
    A naïve approach would involve mapping/unmapping the other task’s stack fully
      Not good for performance or security!
    The PRIVATE KSTACKS feature changes out the backing storage for that stack variable
      A new region for such “nolocal” variables allocation is pointed to by the associated task struct
      This allows the output buffer to be visible to the workthread task
        Without any performance-affecting map/unmap operations

## Slide 54: PaX/grsecurity PRIVATE KSTACKS
Contemporary systems usually consist of multiple CPU cores executing processes in parallel
Due to a multitasking nature of OSes, these processes are constantly being scheduled and preempted
  Usually there is more processes than CPU cores and all of them must receive CPU time
  Process context switching involves page tables switching
    … and usually requires some translations invalidation
  Resumed processes might not continue execution on the same CPU
    TLB Shootdown to keep translation caches coherent might be needed

## Slide 55: PaX/grsecurity PRIVATE KSTACKS
With PRIVATE KSTACKS feature all-but-current process stacks are not mapped
  Upon process context switch the preempted process’ stacks needs to be unmapped and a new process stack mapped
    That involves page table entries modifications as well as TLB invalidation
  Here, it also involves all kernel context stacks on and during every context switch
  A meticulous selection of stacks allowed to be mapped is also needed
A naïve implementation of this feature could involve a lot of page table operations leading to complex and expensive TLB maintenance requirements
The actual PRIVATE KSTACKS feature implementation uses various techniques, that significantly reduce this complexity and cost  limiting the TLB invalidation requirements to the minimum
  The most important one here: optimized page tables
    Minimizing amount of mapping tables for each page table level
    Page table re-use for kernel stacks mapping during context switching

## Slide 56: PaX/grsecurity PRIVATE KSTACKS
Quite a while after the feature had been completed we started to observe weird things…
  Rare, but reproducible #PF exceptions during process context switches
    Always involving previous and next kernel stacks pages accesses
    Impossible to explain based on preceding page tables operations and page tables content
    Spurious in nature… just ignoring them was enough to restore proper execution
      That suggested: no error in page tables, everything was mapped as expected
    Never reproducible in virtualized environment (from within a VM)
    Seemingly only reproducible on back-then new Intel CPUs of Alderlake family
      These CPUs consists of so called P-cores (performance ones) and E-cores (slower ones)
      The problem seemed to be bound to the E-cores only
  Super rare (a handful of occurrences) RAP violations - indicating kernel stack data corruption
    Impossible to explain and completely indeterministic

## Slide 57: PaX/grsecurity PRIVATE KSTACKS
How do you debug a bug that makes no sense?
A lot of hours spent reproducing, limiting scope, narrowing down, tracing, documentation reading…
Finally, at some point, we noticed a pattern
  Always two re-used and consecutive 2nd level page tables were involved
    New: currently mapped and previously unmapped
    Old: currently unmapped and previously mapped
    Both of the page table addresses had same bits 47:21
  The #PF always involved a kernel stack address, whose page table entries indicated:
    It is currently mapped using the new 2nd level page table entry
    It was mapped just before when using the old 2nd level page table entry
    It is not mapped (present) currently when using the old 2nd level page table entry

## Slide 58: PaX/grsecurity PRIVATE KSTACKS – Page Tables (Before)

## Slide 59: PaX/grsecurity PRIVATE KSTACKS – Page Tables (After)

## Slide 60: PaX/grsecurity PRIVATE KSTACKS
That rang a bell…
  The paging-structure caches might be at play here…
  Also, we weren’t able to reproduce in a VM…
    … and VMX transitions do flush the paging-structure caches
But why?
  The spurious nature of the #PF indicated that there was no mistake in page tables:
    Previously unmapped page does not need invalidation as non-present pages translations are not cached
  There was no architectural memory access that could potentially populate the translation caches with previously unmapped 2nd level page table
  CPUs of other microarchitectures did not exhibit this problem at all

## Slide 61: PaX/grsecurity PRIVATE KSTACKS
Then a couple of documentation snippets caught our eye:
  “The use of the PDE cache depends on the paging mode: [...] For 4-level paging, each PDE-cache entry is referenced by a 27-bit value and is used for linear addresses for which bits 47:21 have that value”
  “The processor may create an entry in a paging-structure cache even if there are no translations for any linear address that might use that entry. Thus, if software has marked “not present” all entries in a page table, the processor may subsequently create a PDE-cache entry for the PDE that references that page table (assuming that the PDE itself is marked “present”).”
  “The processor may create entries in paging-structure caches for translations required for prefetches and for accesses that are a result of speculative execution that would never actually occur in the executed code path.”
  “If the processor does not find a relevant TLB entry, it may use the upper bits of the linear address to select an entry from the PDE cache that is associated with the current PCID (Section 4.10.3.1 indicates which bits are used in each paging mode). It can then use that entry to complete the translation process (locating a PTE, etc.)”

## Slide 62: PaX/grsecurity PRIVATE KSTACKS
That made us develop a hypothesis:
  What if Alderlake CPUs’ E-Cores are more “sensitive” and more likely to create and retain paging-structure caches entries…
  … even for the no-translations-requiring page tables…
  … merely based on a specific page table pages re-use and access patterns specific to the PRIVATE KSTACKS feature?

## Slide 63: PaX/grsecurity PRIVATE KSTACKS
More specifically, what if the following happens:
  Previous kernel stack page is unmapped and its translations are invalidated
  Current (new) kernel stack page becomes mapped, but does not have any entries in TLB (yet)
  The previously used and now unmapped 2nd level page table’s entry remains in paging-structure cache
    It has the same indexing bits as the new page table page
  When a new kernel stack access triggers a page walk, it uses stale entry from the paging-structure cache
    When such misdirected page walk returns a non-present previous kernel stack’s entry:
      #PF exception is thrown
    When such misdirected page walk returns a present kernel stack’s entry:
      A stack data corruption can happen…
        … leading to the unexplainable RAP violations we used to observe

## Slide 64: PaX/grsecurity PRIVATE KSTACKS – Proof-of-Concept
Let’s test the hypothesis with a PoC…
The PoC presented here is a simplified approximation of the chain of events, that happen during the PRIVATE KSTACKS context switch and that could lead to the unexpected #PF exceptions
Primary objectives of the PoC were:
  Prove paging-structure cache involvement and anticipated behavior
  Prove the “uniqueness” of the Intel Alderlake CPUs
    Same PoC should reproduce only of these CPUs
  Reproduce the issue inside a VM, by better controlling of VMX transitions occurrences
  Help to develop best (performance-wise) fix for the issue

## Slide 65: PaX/grsecurity PRIVATE KSTACKS – Proof-of-Concept
The PoC begins by selecting two arbitrary virtual addresses to become the bases of two distinct address spaces
Then, we allocate and map in the first address space, which consists of 502 consecutive 4K pages

## Slide 66: PaX/grsecurity PRIVATE KSTACKS – Proof-of-Concept
Next, we allocate and map in the second address space, which consists of 512 consecutive 4K pages
  A full 2MB range
Then, we obtain 2nd level page table entries for both of the base addresses and make a backup of the default content for the second address’ entry

## Slide 67: PaX/grsecurity PRIVATE KSTACKS – Proof-of-Concept
Now, we can predict the virtual address of the expected spurious #PF
  It is an address of the first unmapped page from the 2MB range of the first address space
    Remember: we only mapped in 502 of 4K pages

## Slide 68: PaX/grsecurity PRIVATE KSTACKS – Proof-of-Concept
Finally, by running the main loop, we should be able to trigger the predicted spurious #PF exception
  The loop does the following…
  At its second iterations, we should hit the paging-structure cache collision…

## Slide 69: PaX/grsecurity PRIVATE KSTACKS – Proof-of-Concept
And there we have it!

## Slide 70: PaX/grsecurity PRIVATE KSTACKS – Proof-of-Concept
Summary:
  The higher-level page table entries can be cached in paging-structure caches whenever CPU decides to do so
  When aliasing and/or collision in translation caches can occur: invalidation is a must
    That’s why Intel SDM recommends the “at least one INVLPG instruction” invalidation
  Otherwise page walk can be optimized and bad things could happen

## Slide 71: Broken INVLPG instruction on Intel Gracemont microarchitecture

## Slide 72: Broken INVLPG instruction case
Around the same time, a FreeBSD received a bug report
  261169 – Intel Alder Lake: data corruption with Read&Write files to FAT32 or UFS

## Slide 73: Broken INVLPG instruction case
Some time later FreeBSD received a fix for the issue:
  https://cgit.freebsd.org/src/commit/?id=cde70e312c3fde5b37a29be1dacb7fde9a45b94a

## Slide 74: Broken INVLPG instruction case
What does the fix do?
Replaces INVLPG instruction usage with INVPCID, because the INVLPG instruction apparently does not flush all global TLB entries when PCID is enabled!
  Despite it should!

## Slide 75: Broken INVLPG instruction case
Then, Intel publishes an erratum for the affected processors:
  Errata Details - 027 - ID:682436 | 12th Generation Intel® Core™ Processor

## Slide 76: Broken INVLPG instruction case
The plot thickens…
  Intel confirmed the incorrect behavior of INVLPG instruction, but also …
  Intel mentioned that the INVLPG instruction only fails to flush global TLB entries when PCID is enabled and outside of the VMX virtualized environment!
What was the natural conclusion?
  That this was the same bug we were having with PRIVATE KSTACKS
    There were just too many coincidences…

## Slide 77: Broken INVLPG instruction case
But, there was also a couple of serious “buts”…
  The PCID being enabled or disabled did not play a role for the PRIVATE KSTACKS bug at all
  And more importantly: unlike FreeBSD, we do not use global pages!
After a careful investigation we were able to conclude that these were indeed two completely separate issues!
  One was just a counter-intuitive corner case scenario resulting from specification ambiguity…
    … and opaque new hardware microarchitectural modifications!
  The other was just a new hardware CPU bug!
A classic situation where nothing is what it seems…

## Slide 78: Conclusions
Maintaining coherency between page tables in memory and CPU translation caches is complex
  Even if only correctness is kept in mind
  It becomes much harder when optimizing for performance
Documentation is ambiguous, imprecise and lacks important details
  Probably on purpose: vendors do not want to reveal implementation details
Sometimes, something that seems to be a CPU bug, is just a convoluted, counter-intuitive and super rare corner case scenario manifestation
Other times, the convoluted, counter-intuitive and super rare corner case scenario manifestation is nothing but a CPU bug
No magic wand

## Slide 79: Thank you
wipawel@grsecurity.net